## Slide 1
Introduction to Networking
and the Wireless Edge
AI-Edge summer REU program
Jim Kurose
University of Massachusetts, Amherst

## Slide 2
Overview of today’s REU seminar
Networking 101 - in 10 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 3: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  running Internet applications
  clients, servers
  5.3 B Internet users (2024)
Networks
  collection of devices, routers, links: managed by an organization

## Slide 4: What is the Internet: a “nuts and bolts” view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
user devices at network edge: clients
servers often in data centers

## Slide 5: Internet-connected devices (not just computers)
Web-enabled toaster +
weather forecaster
Internet phones
Slingbox: remote
control cable TV
Security Camera
IP picture frame
Internet
refrigerator
Tweet-a-watt:
monitor energy use
Amazon Echo
Gaming devices
Pacemaker & Monitor
diapers
cars
scooters
sensor
AR devices
Fitbit
laptop
bikes
wireless and mobile devices

## Slide 6
What is the Internet: a “nuts and bolts” view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network core:
  interconnected regional, national, global Internet Service Providers (ISPs): AT&T, Sprint, Level-3, NTT
  interconnected global company networks (e.g., Google, Facebook)
Network edge:
devices, servers connect directly to access networks: (Comcast, Verizon, UMass, company networks)
Network devices:
user devices: aka “clients”
servers often in data centers

## Slide 7: Packet switching
hosts break application-layer messages into packets
network forwards packets from one router to the next, across links on path from source to destination
destination re-assembles packets into application message
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
4 3 2 1

## Slide 8: Wireless and Mobile Networks: context
more mobile-broadband-connected (cellular) devices than fixed-broadband-connected devices devices (5-1 in 2025)!
  wireless connectivity even great when WiFi users considered (80% of broadband homes use WiFi)
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
1000
2000
3000
4000
5000
6000
7000
8000
Mobile broadband subscribers (M)
Fixed (wired) broadband subscribers (M)
Broadband subscribers (M)
Data source: www.statista.com (1/25)
2023

## Slide 9: Wireless and Mobile Networks: context
% global website traffic generated by mobile devices (excluding tablets)
Image source: www.statista.com (11/23)
Majority of Internet web site traffic directed to mobile (rather than fixed) devices

## Slide 10
Wireless applications their needs
Six application areas :
Wide-area Mobile Wireless Internet Access
Local-area Mobile Wireless Internet Access
Fixed Wireless Internet Access
Satellite Networks for Internet Access and Sensing
Cable replacement
Internet of Things (IoT)
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
Application needs:
mobility
user data rate
energy efficiency
device density
latency
area traffic capacity

## Slide 11
device ranges over tens or hundreds of miles while maintaining continuous Internet connectivity (e.g., VoIP, streaming, ongoing TCP connection)
only provided by cellular networks
Wide-area Mobile Wireless Internet Access
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
wide-area mobile Internet access
Q: two high importance, 1 medium/low importance

## Slide 12
connecting devices (often small, energy-constrained) to computation that senses, monitors, reports, and controls phenomena in the physical world
Bluetooth, WiFi, cellular, LoRaWAN
Internet-of-Things
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
Internet of Things
Q: two high importance, 1 medium/low importance

## Slide 13
Overview of today’s REU seminar
Networking 101 - in 10 minutes
Wireless networks: motivation, applications
Elements of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 14: Elements of a wireless network
wired network
infrastructure

## Slide 15: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 16: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., 4G/5G cell towers, 802.11 (WiFi) access points (APs)

## Slide 17: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect device(s) to base station, also used as backbone link
multiple access protocol coordinates link access (random access, FDMA, TDMA, CDMA, polling)
various transmission rates and distances, frequency bands
Ad hoc networks: not all wireless networks are connected into a larger network

## Slide 18: Elements of a wireless network
wired network
infrastructure
wireless device radio
wireless device has different radios for different networks
iPhone16: has ~11 different radios, many antennae
  5 different cellular radios, WiFi, Bluetooth, UWB, satellite NFC, GPS
Notes: 5G NR (New Radio): Supports both Non-Standalone (NSA) and Standalone (SA) modes, encompassing sub-6 GHz and mmWave frequencies for high-speed data transmission.
LTE (Long-Term Evolution): Includes support for both Frequency Division Duplexing (FDD) and Time Division Duplexing (TDD) variants, facilitating widespread 4G connectivity.
WCDMA (Wideband Code Division Multiple Access): Provides compatibility with 3G networks, ensuring service continuity in areas where newer technologies are unavailable.
HSPA+ (Evolved High-Speed Packet Access): Enhances 3G network performance, offering faster data rates and improved efficiency.
GSM (Global System for Mobile Communications): Ensures basic voice and data services, particularly in regions where GSM remains prevalent.

## Slide 19: Wireless networks: radio
Wireless radio
signal carried in various “bands” in electromagnetic spectrum
no physical “wire”
broadcast, “half-duplex” (sender to receiver)
propagation environment effects
  reflection
  obstruction by objects
  interference/noise
Radio link types:
Wireless LAN (WiFi)
  10-1000’s Mbps; 10’-100s of meters
wide-area (e.g., 4G/5G cellular)
  10’s Mbps over ~10 Km
  Gbps over short distances (mmwave)
Bluetooth: cable replacement
  short distances, limited rates
satellite
  geostationary: < 45 Mbps per channel, 270 msec e-e delay
  LEOS: 50-100 Mbps downlink (Starlink), 46 msec LEOS
Notes: Recent Starlink speeds: https://arstechnica.com/tech-policy/2022/09/ookla-starlinks-median-us-download-speed-fell-nearly-30mbps-in-q2-2022/

## Slide 20: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE, 5G eMBB
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
Space (100’s of Km)
LEOS

## Slide 21: 802.11 (WiFi) LAN architecture (overview)
wireless host communicates with base station
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  wireless channel
  access point (AP): base station
other network services (identity management, IP addressing and routing, DHCP) handled by institutional IP infrastructure: WiFi is a layer-2 (only) network!
BSS 1
BSS 2
institutional
network,
Internet
switch
or router

## Slide 22
Overview of today’s REU seminar
Networking 101 - in 10 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 23
Architectural Elements of 5G
radio access
Network (RAN)
to
Internet
5G core network
gNodeB
User equipment
(UEs)
Core Network Functions

## Slide 24
5G Radio Access Network (RAN)
gNodeB
User equipment
(UEs)
5G RAN: edge network connecting devices (UEs) to base station (gNodeB)
provides link-layer service, as first hop between devices and larger network
limited geographic scope
under control of a single service provider
somewhat analogous to WiFi LAN
RAN components:
  many devices (User Equipment: UE)
  radio channel (New Radio: NR)
  one base station (Next Generation Node B: gNodeB, gNB)

## Slide 25
5G RAN components
gNodeB
User equipment
(UEs)
5G User Equipment (UE):
smartphone, tablet, laptop, IoT device
UEs host, run applications
devices attached in RAN
may or may not be mobile

## Slide 26
5G RAN components
gNodeB
User equipment
(UEs)
Radio Channel (aka New Radio, NR, in 5G)
Physical (PHY) layer: OFDMA
UEs only communicate with base station
  via uplink, downlink channels
  UEs do not communicate directly with each other
various uplink/downlink physical and logical channel defined

## Slide 27
5G RAN components
gNodeB
User equipment
(UEs)
Base station (aka Next Generation Node B (gNodeB or gNB in 5G):
central control point for RAN, role somewhat analogous to that of WiFi AP
computing, storage may be located at gNB
all communication between UEs and other endpoints (other UEs, 5G Core, Internet) go through gNB
aka Extended Node B (eNB) in 4G

## Slide 28
5G Core Network
to
Internet
Core Network Functions
Core situated between RAN and other endpoints (Core, larger Internet)
  single Core; multiple RANs
consist of links, routers, servers, providing services to UEs and gNBs
  “all Internet” Core, but very different services than traditional Internet apps
clear logical separation between control-plane, user plane:
  CUPS: Control-Plane and User-Plane Separation

## Slide 29: 5G control- and user- plane separation (CUPS)
control plane
emphasis on functions and services
well-defined interfaces defines between services
gNB, RAN
N2
N7
N5
N13
N12
N10
N8
N5
N3
N1
N11
base station
(gNB)
S-GW
data plane
5-layer Internet data plane
extensive use of tunneling
IP tunnel
N3
N6
N6
AMF
Access, Mobility
Management
SMF
Session
Management
PCF
Policy control
AUSF
Authentication
Server
UDM
Unified Data Management
AF
Application Function
UPF
User
Plane
IP datagrams

## Slide 30: 5G: Local application breakout, slicing
…
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity (MME)
PDN gateway
(P-GW) and Serving Gateway (S-GW)
to
Internet
…
Mobile device
(UE)
Base station
(gNode-B)
to
Internet
IoT
Multimedia
Video app
IoT app
network slices: allocate resources end-end, segregate traffic to deliver different QoS to a collection of devices, apps
local breakout: enables direct communication between devices, applications without traffic leaving mobile core

## Slide 31: RAN packet processing pipeline: context
Base station
(gNode-B)
IP datagrams
RAN: transfers datagrams between mobile core and UEs
UE
datagrams
protocol processing pipeline in UE

## Slide 32: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
traditional 3GPP view
datagrams
RRC (Radio Resource Control)
configures coarse-grained, policy-related aspects of pipeline (e.g., scheduling prioritization, security)
this implements the RAN’s control plane
does not process user plane packets

## Slide 33: Software-defined RAN
Recall our earlier description of traditional RAN base station (below)
tightly coupled control and data planes
let’s focus on control / management: RRC implementation

## Slide 34: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
3GPP-compliant interface between RAN and Mobile Core control plane
New programmatic API for exerting software-based control over pipeline that implements RAN user plane
Re-factored RRC
SDN-controlled switches

## Slide 35: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
Re-factored RRC
SDN-controlled switches
RAN Network Information Base (R-NIB)
common set of information consumed by numerous control apps, e.g., longer time-scale CQI (channel Quality Indicator) values, other per-session state
R-NIB
load
balancing
handover
QoS
Near-real time network control applications implemented as “xApps”
…
…

## Slide 36: Mobility in 5G networks: major mobility tasks
Visited network
Streaming server
Home
network
Internet
1
3
4
association:
covered earlier
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
AMF, visited UDM, home UDM establish control-plane state: mobile in visited network
2
data-plane configuration:
AMF, SMF configures forwarding tunnels
visited, home network establish tunnels from home to mobile, only if home-routed
3
mobile handover:
mobile device changes its point of attachment to visited network
4
AMF
AUSF
SMF
PCF
UDM
SEPP
1
AMF
AUSF
SMF
PCF
UDM
SEPP
2