## Slide 1
Software-i-zation and AI
at the wireless edge
AI-Edge summer REU program
Jim Kurose
University of Massachusetts, Amherst

## Slide 2
Overview of today’s REU seminar
wireless (5G, nG) networks: review
network software-i-zation
three 5G/nG network control/management challenges
... and opportunities for AI/ML
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 3
Architectural Elements of 5G
radio access
Network (RAN)
to
Internet
5G core network
gNodeB
User equipment
(UEs)
Core Network Functions

## Slide 4
5G Radio Access Network (RAN)
gNodeB
User equipment
(UEs)
5G RAN: edge network connecting devices (UEs) to base station (gNodeB)
provides link-layer service, as first hop between devices and larger network
limited geographic scope
under control of a single service provider
somewhat analogous to WiFi LAN
RAN components:
  many devices (User Equipment: UE)
  radio channel (New Radio: NR)
  one base station (Next Generation Node B: gNodeB, gNB)

## Slide 5
5G RAN components
gNodeB
User equipment
(UEs)
5G User Equipment (UE):
smartphone, tablet, laptop, IoT device
UEs host, run applications
devices attached in RAN
may or may not be mobile

## Slide 6
5G RAN components
gNodeB
User equipment
(UEs)
Radio Channel (aka New Radio, NR, in 5G)
Physical (PHY) layer: OFDMA
UEs only communicate with base station
  via uplink, downlink channels
  UEs do not communicate directly with each other
various uplink/downlink physical and logical channel defined

## Slide 7
5G RAN components
gNodeB
User equipment
(UEs)
Base station (aka Next Generation Node B (gNodeB or gNB in 5G):
central control point for RAN, role somewhat analogous to that of WiFi AP
computing, storage may be located at gNB
all communication between UEs and other endpoints (other UEs, 5G Core, Internet) go through gNB
aka Extended Node B (eNB) in 4G

## Slide 8
5G Core Network
to
Internet
Core Network Functions
Core situated between RAN and other endpoints (Core, larger Internet)
  single Core; multiple RANs
consist of links, routers, servers, providing services to UEs and gNBs
  “all Internet” Core, but very different services than traditional Internet apps
clear logical separation between control-plane, user plane:
  CUPS: Control-Plane and User-Plane Separation

## Slide 9
5G Core Network
to
Internet
Core Network Functions
Core situated between RAN and other endpoints (Core, larger Internet)
  single Core; multiple RANs
consist of links, routers, servers, providing services to UEs and gNBs
  “all Internet” Core, but very different services than traditional Internet apps

## Slide 10
Architectural Elements of 5G
radio access
Network (RAN)
to
Internet
5G core network
gNodeB
User equipment
(UEs)
Core Network Functions
AMF (Access, Mobility Management Function)
connection management, access authorization
mobility management

## Slide 11: Mobility in 5G networks: major mobility tasks
Visited network
Streaming server
Home
network
Internet
1
3
4
association:
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
AMF, visited UDM, home UDM establish control-plane state: mobile in visited network
2
data-plane configuration:
AMF, SMF configures forwarding tunnels
visited, home network establish tunnels from home to mobile, only if home-routed
3
mobile handover:
mobile device changes its point of attachment to visited network
4
AMF
AUSF
SMF
PCF
UDM
SEPP
1
AMF
AUSF
SMF
PCF
UDM
SEPP
2

## Slide 12
Overview of today’s REU seminar
Wireless (5G, nG) networks: review
network software-i-zation
Three 5G/nG network control/management challenges
... and opportunities for AI/ML

## Slide 13: 5G: migration away from “protocols” is underway!
5G: microservice-like architecture
public Internet
and
inter-carrier IPX
Mobility Management Entity (MME)
PDN gateway (P-GW)
Serving gateway (S-GW)
public Internet
and
inter-carrier IPX
Home Subscriber Service (HSS)
4G mobile core:
boxes and protocols
SDN 13
Notes: a clear migration away from protocols is also clear in the transition from 4G to 5G
I like to think of 4G in terms of boxes and protocols. The green path here is the user plane (IP packets flow to/from the UE device from/to Internet), and the blue interactions are the control and management plane in 4G that control and configure the user-plane devices. 4G: boxes and protocols.
This 5G figure is from the 2018 ITU-T spec Y.3102, which describes the first key feature of an IMT-2020 network as
“distributed architecture based on softwarize-d network functions”
ITU specs discuss the mobile core in terms of software functions. And while it doesn’t mandate a cloud-based SDN-like solution, this diagram is certainly evocative of that. So in some sense we have the 5G physical network infrastructure, and then
we have the management and control of these
SEGUE: Those of you who watch this space commercially probably saw the

## Slide 14: 5G: migration away from “protocols” is underway!
5G: microservice-like architecture
public Internet
and
inter-carrier IPX
Note: 4G/5G operators manage intradomain services in their mobile network
SDN 14
Notes: Software companies and operators coming together
Segue: SO ... given these changes are underway in SD_WAN, in 4G-5G, does this mean protocols are dead?
Here are the insights that I’ve drawn when thinking about this question “Are protocols dead”?

## Slide 15: 5G: software-i-zation: Core
…
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity (MME)
PDN gateway
(P-GW) and Serving Gateway (S-GW)
to
Internet
…
Mobile device
(UE)
Base station
(gNode-B)
to
Internet
PCF
Policy control
AMF
Access, Mobility
Management
AUSF
Authentication
Server
AMF
Access, Mobility
Management
SMF
Session
Management
PCF
Policy control
UPF
User
Plane
NEF
Network Exposure
AF
Application Function
NRF
Network Repository
UDM
Unified Data Management
from 4G boxes
to 5G
functions and services
software defined networking (SDN): 5G microservices can be implemented in data centers
cloud infrastructure within the mobile 5G network

## Slide 16: 5G: software-i-zation: RAN
Recall our earlier description of traditional RAN base station (below)
tightly coupled control and data planes
let’s focus on control / management: RRC implementation
RAN: transfers datagrams between mobile core and devices

## Slide 17: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
3GPP-compliant interface between RAN and Mobile Core control plane
New programmatic API for exerting software-based control over pipeline that implements RAN user plane
Re-factored RRC
SDN-controlled switches

## Slide 18: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
Re-factored RRC
SDN-controlled switches
RAN Network Information Base (R-NIB)
common set of information consumed by numerous control apps, e.g., longer time-scale CQI (channel Quality Indicator) values, other per-session state
R-NIB
load
balancing
handover
QoS
Near-real time network control applications implemented as “xApps”
…
…

## Slide 19
Overview of today’s REU seminar
Wireless (5G, nG) networks: review
network software-i-zation
Three 5G/nG network control/management challenges
... and opportunities for AI/ML

## Slide 20: Challenge 1: Mobility in 5G networks: handover
Handover:
mobile device changes is point of attachment to the network
data flow to device changes from source base station to target base station
AMF
Access, Mobility
Management
SMF
Session
Management
UPF
User Plane Function
before
handover
after
handover
Why perform handover?
stronger signal from target base station
target base station has less devices, less traffic

## Slide 21
source BS
1
3
2
data path before handover
data path after
handover
1
current (source) BS selects target BS, sends Handover Request message to target BS
2
target BS pre-allocates radio time slots, responds with HR ACK with info for mobile
3
source BS informs mobile of new BS
mobile can now send via new BS - handover looks complete to mobile
4
source BS stops sending datagrams to mobile, instead forwards to new BS (who forwards to mobile over radio channel)
target BS
4
UPF
User Plane Function
Challenge 1: Mobility in 5G networks: handover

## Slide 22
UPF
User Plane Function
source BS
target BS
5
5
target BS informs AMF, SMF that it is new BS for mobile
SMF instructs UPF to change tunnel endpoint to be (new) target BS
AMF
Access, Mobility
Management
SMF
Session
Management
6
UPF
User Plane Function
6
target BS ACKs back to source BS: handover complete, source BS can release resources
7
mobile’s datagrams now flow through new tunnel from target BS to UPF
5
Challenge 1: Mobility in 5G networks: handover

## Slide 23
Handover in 5G networks: how AI/ML can help
?
User behavioral patterns can be learned/predicted:
where are users likely to move in future
future communication (bandwidth) requirements
per-RAN predictions of bandwidth requirements of users in aggregate
These predictions can be used in
handover: where/when to perform handover?
quality of service (QoS): what near-term-future quality of service guarantees can be made to a user

## Slide 24
antenna performance to a given location is a complex, time-varying quantity due to
  reflections (multipath)
  Interference
MIMO: multiple antennas
single user MIMO
multi-user MIMO
Challenge 2: beam (antenna) allocation/steering
How AMI/ML can help:
antenna performance can be measured, future antenna performance predicted
outputs from ML prediction model used to steer antennas to optimize performance

## Slide 25
Base station
(gNode-B)
RAN: transfers datagrams between mobile core and UEs
UE
datagrams
protocol processing pipeline in UE
Challenge 3: packet scheduling in RAN
datagrams

## Slide 26: 5G RAN scheduling: Channel Quality Indicator
Channel Quality Indicator (CQI):
device measures quality of received reference signals reports quality to base station
4-bit CQI value tells base station how fast it can transmit (bad channel: transmit slow)
“We are all equally important”
CQI
Notes: Well, I’ve just said that a MAC scheduler may take the quality of the channel between the bases station and UE into account when making a scheduling discipline. In the next lesson of this module, we’ll look at how a UE and base station actually determine the quality of the channel.
<ANIMATE 1> But for now, I’ll just point out that the UE is going to periodically send a 4-bit Channel Quality Indicator - CQI – to the gNodeB. The gNB, in turn, uses the CQI to determine which modulation scheme to use.
<ANIMATE 2> Indeed, here’s the 4-bit CQI table from the standards that maps a CQI value onto a modulation scheme.
Different modulation schemes mean different numbers of bits per second that are being transmitted. Different throughput. Higher order QAM means higher throughput.
As we’ll see there are MAC scheduling disciplines that use this CQI in determining frame transmission order.

## Slide 27: 5G RAN scheduling: QoS Class Indicator
QCI: QoS Class Indicator
QoS: network wants to provide to a particular device (e.g., delay, guaranteed bit rate QoS guarantees)
scheduler determines channel allocation to ensure all devicesmeet their QoS requirements
Priority | QCI | Max delay | Max loss | Application
2 | 1 | 100ms | .01 | Voice
3 | 4 | 50 ms | .001 | Real-time gaming
6 | 7 | 300 ms | .000001 | Streaming video
8 | 8 | 600 | .000001 | Web browsing, TCP
CQI
QCI
Notes: There is a second piece of information that is also sometimes used by MAC scheduling disciplines. It’s called the
the Quality of Service Class indicator – which unfortunately has an acronym (QCI) which is easily confused with CQI that we just studioed
<ANIMATE 1> In some cases, the network may promise a certain quality of service (QOS) to a UE. We’ll study QOS in later module. But the basic idea is that a UE may need a certain level of performance in order for the network to be useful for a given application. For example, for real-time interactive voice, you need short delays. In such cases, the network can make a quality of service guarantee to the UE that it, the network, will need to meet through it’s allocation of resources, allocation of RBs.
<ANIMATE 2> But, for now, we only need know that a MAC scheduler can also take the QOS Class indicator into account when making scheduling disciplines.
Again, the standards don’t say how the scheduler should make QoS-sensitive decisions,
<ANIMATE 3> but it does standardize that there is a 3bit QCI
which has the semantics shown here

## Slide 28: 5G MAC scheduling disciplines
Q: what algorithm does scheduler use to choose frame data to be sent into N blocks?
Link-layer frame data awaiting transmission
Channel blocks that will carry frame data destined to specific devices
Scheduler
CQI
QCI
Scheduling: which frame(s) to schedule for transmission
performance will depend on channel conditions, user device
Notes: Here’s the common framework for all of the scheduling disciplines we’ll study.
<ANIMATE 1>. At each scheduling instant, we’re given a group of frames that are queued at the base station, awaiting transmission to the UEs. The frames can contain all different types of traffic. There can be data, control and management frames. There can be all sorts of application-layer data: voice, video, web browsing. You name it!
Note that we’ve shown 6 different queues here, each in a different color. Perhaps these are queues for 6 different UE’s (that’s the easiest way to think about it), but it could be queues for six different classes of traffic. The standards don’t say – this whole discussion is beyond the standards. But let’s just think of these as per-UE queues.
To simplify things, let’s also assume that each of these colored squares have just enough data to fill a resource block. We know that’s not true since we know that the number of bits that fill an RB will depend on the modulation scheme being used. But it’ll be good enough for explaining scheduling disciplines.
<ANIMATE 2>. Then we have the scheduler, which may have per-UE channel quality information (QCI) and per-frame Quality of Service Class Indications (QCIs)
<ANIMATE 3> And then we have the set of resource blocks that will be used between now and the next scheduling instant; these are the RBs to be scheduled and that will carry frame data destined to the UE’s.
And here’s the million dollar question: what algorithm does scheduler use to choose frame data to be packed into say N resource blocks?

## Slide 29
Packet scheduling in RAN: how AI/ML can help
Transmission performance can be learned / predicted for each packet, depending on:
channel conditions
UE mobility
These predictions can be used to determine expected per-packet transmission performance
actual packet selected depends on many factors: performance, fairness, quality of service

## Slide 30
Summary/Conclusions
Last week:
Networking 101 - in 20 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
This week:
wireless (5G, nG) networks: review
network software-i-zation
three 5G/nG network control/management challenges
... and opportunities for AI/ML
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking
Enjoy this summer REU!